## Slide 1
PRCP
IRG
SNOWW
CANOPYW
GW
Tavg
LAI
SOILW:
9 active layer (0-4 m)
1 boundary layer (4-10m)
prcp_to_snoww
prcp_to_canopyw
prcp_to_soilSurface
snoww_subl
snoww_to_soilw
canopywEvap
pondwEvap
soilwEvap
canopyw_to_soilw
prcp_to_Hrunoff
deep_percol
deep_diffus
percol[10]
diffus[10]
PONDW
Gwmovchange[10]
GW_to_pondw
Gwdischarge[10]
Gwrecharge[10]
pondw_to_Drunoff
soilw_to_pondw
soilwTransp[10]
IRG_to_soilw
IRG_to_prcp
IRG
height
pondw_to_soilw
RCN

## Slide 2: Legend
Boudary conditions (input data) – green ellipse
PRCP: daily sum of precipitation
IRG: amount of irrigated water (height → above or below canopy)
GW: groundwater (GWD: groundwater depth – if positive: below surface, if negative: above surface-waterlogging)
  CF: capillary fringe – capillary zone
  GWeff: saturation effect of groundwater (-9999: normal zone, 0: CF, 0-1: in GW-layer, 1: below GW)
Input fluxes – blue arrows
IRG_to_prcp: irrigatied water amount above canopy height
IRG_to_soilw: irrigatied water amount below canopy height
prcp_to_snoww: snowpack accumulation
prcp_to_canopyw: interception on canopy
prcp_to_soilSurface: precipitation reaching souil surface (pondw or top soil layer)
Output fluxes – yellow arrows
prcp_to_Hrunoff: Hortonian runoff flux (no real output: calculation before RPCP enters into system based on RCN)
snoww_subl: sublimation from snowpack
snoww_to_soilw: melt from snowpack
pondw_to_Drunoff: Dunnian runoff flux from pondw
canopyw_EVP: evaporation from canopy
canopyw_to_soilw: canopy drip and stemflow (no canopyw at the end of the simulation day (canopyw_to_soilw =prcp_to_canopyw – canopywEVP)
pondwEVP: pond water evaporation based on potEVP (potential evaporation: potEVP >= soilwEVP + pondwEVP)
soilwEVP: evaporation from soil based on potEVP (potential evaporation: potEVP >= soilwEVP + pondwEVP)
soilwTRP[10]: transpiration from the 10 soil layers based on soilwTRPdemand_SUM (transpiration demand for the whole soil system)
Internal fluxes – grey arrows
pondw_to_soilw: water flux from pond to soil
soilw_to_pondw: flux from soil to pond (oversaturation)
GW_to_pondw: water flux from groundwater to pondw
GWdischarge[10]: soil water plus from groundwater (in GW-layers, source of diffusion, evaporation and transpiration is GW)
GWrecharge[10]: recharge: soil water to groundwater (in GW-layers and saturated CF-layers – drainage)
GWmovchange[10]: water change due to the movement of GW
wflux: water flux between soil layers - signed sum (downward: positive, upward: negative) of percolation (percol) and diffusion (diffus);
Others:
VWC – volumetric water content
SAT: saturation
FC: field capacity
WP: wilting point
zlow: lower boundary of soil layer
zup: upper boundary of soil layer
dz: thickness of soil layer
RCN: runoff curve number
LAI: leaf area index
Tavg: averaged daily air temperature

## Slide 3: Sequence of routines
8. soilEVP_calc
limitation and update topsoil layer
Gwdischarge: if GWeff = 1
9. multilayer_transpiration
soilwTRP: soilwTRPdemand_SUM, rootlength_prop
GWdischarge : if GWeff = 1
10. pondANDrunoffD
PONDW update with soilw_to_pondw
Dunnian runoff: pondmax
PONDW update
GW-recharge - waterlogging
PONDW update
11. groundwaterT_CFcharge
if GW and CF are in the same layer, GW-zone fills the capillary zone in the same layer
dz0 = GWD – CFD
VWC0 = VWCorig, VWC0_sat = VWCsat, VWC0_fc = VWCsat
dz1 = soillayer_depth - GWD
VWC1 = VWCsat
VWC1_sat = VWCsat
VWC1_fc = VWCsat
if GW is below 10, but CF is in the bottom layer, GW-zone fills the capillary zone
dz0 = soillayer_depth - CFD
VWC0 = VWCorig, VWC0_sat = VWCsat, VWC0_fc = VWCsat
dz1 = soillayer_depth - CFD
VWC1 = VWCsat, VWC1_sat = VWCsat, VWC1_fc = VWCsat
1. irrigation
IRG_to_prcp (above canopy)
IRG_to_soilSurface (below canopy)
IRG_to_soilw (into the soil)
SOILW update (is saturation: PONDW update)
1. prcpANDrunoffH
prcp_to_snoww
prcp_to_canopyw
prcp_to_runoff
prcp_to_soilSurface
2. snowmelt
snoww_to_soilw
snoww_subl
no update
3. canopy_et
soilwTRPdemand_SUM
canopywEVP
canopyw_to_soilw
no update
4. pontential_evap
potEVP
no update
5. groundwaterT_preproc
GWD, CWD
Gwlayer, CFlayer
GWmovchange[10]: soilw update – if GWD ≠ preGWD
Gwdischarge[Gwlayer]: if VWC<VWCfc → VWC=VWCfc
GW_waterlogging (negative GWD data)
GWeff[10]: (zlow-GWD)/dz
6. infiltANDpond
waterFromAbove = prcp_to_soilSurface + snoww_to_soilw + canopyw_to_soilw + IRG_to_soilSurface
soilwEXTRA: amount of water which can still fits into the soil
pondw_to_soilw:based on PONDW and soilwEXTRA
PONDW update
infiltPOT
pondwEVP
  PONDW update, soilwEVP udapte if necessíary (potEVP)
soilw_to_pondw (waterFromAbove > soilwEXTRA)
7. tipping
percol: based on DRAIN
GWeff > 0: percol=0
saturation: Gwrecharde=DRAIN, percol=0
diffus
GWeff[layer+1] =1: Gwdischarge = diffus[layer]
wflux=percol+diffus
special bottom boundary layer:
wflux[10]=wflux[9]